## Slide 2
International Union of Geological Sciences
Manual of Standard Methods
for
Establishing the Global Geochemical Reference Network
Chapter 3.3
Stream Water Sampling
Timo Tarvainen1,4, Tarja Hatakka1, Mikael Eklund1, Reijo Salminen1,
Christopher C. Johnson2,4, Alecos Demetriades3,4
1 Geological Survey of Finland, Espoo, Finland
2 GeoElementary, Derby, United Kingdom,
3 Institute of Geology and Mineral Exploration (retired), Athens, Hellenic Republic
4 IUGS Commission on Global Geochemical Baselines
Tarvainen, T., Hatakka, T., Eklund, M., Salminen, R., Johnson, C.C. & Demetriades, A., 2022. Stream Water Sampling. Chapter 3.3 In: Demetriades, A., Johnson, C.C., Smith, D.B., Ladenberger, A., Adánez Sanjuan, P., Argyraki, A., Stouraiti, C., Caritat, P. de, Knights, K.V., Prieto Rincón, G. & Simubali, G.N. (Editors), International Union of Geological Sciences Manual of Standard Methods for Establishing the Global Geochemical Reference Network. IUGS Commission on Global Geochemical Baselines, Athens, Hellenic Republic, Special Publication, 2, 207−227.
It is recommended that reference to this part of the Manual should be made in the following way:

## Slide 3
Stream water samples are collected from second order drainage basins

## Slide 4
Flowing stream water is collected from a small, second-order, drainage basin (<100 km2; at the same site as active stream sediment.
In semi-dry and dry terrains, such as southern Europe, North and South Africa, Namibia, parts of North, Central and South America, Australia, and other countries with dry late spring, summer and early autumn seasons, streams may not have flowing water if sampling is carried out during these periods, yet ponds with stagnant water may be found. No samples should be collected from such ponds, since the geochemistry of stagnant water is normally different from that of flowing stream water.
3.3.2. Stream water sampling
In true humid tropical and temperate climates, streams will rarely run dry and there is always an abundance of water. However, the wettest time of the year should be avoided in order not to sample during periods of high rainfall and flood events when the stream water is diluted with substantial surface water run-off. Ideally, stream water samples should not be collected within forty-eight hours of a rainfall event in the selected second-order catchment basin. If this is not possible, the time of the rainfall event should be recorded on the field observations sheet.
Continued…..

## Slide 5
3.3.2. Stream water sampling
…..Continued…..
If the sampling campaign is to be carried out over several years, it is important to collect the stream water samples during the same climatic season. Other parameters to be considered are the transient character of stream water chemical composition, and that element concentrations are susceptible to various sources of temporal variation. Thus, the generated data are ‘snapshots’ of the chemical state of stream water at the time of sampling (Lark et al., 2016). These authors recommend setting up monitoring sites on selected streams, where daily stream water samples are collected over variable time intervals. The statistical analyses of water geochemical data from these monitoring sites can supplement the results from the analysis of routine stream water samples, collected in a once-off sampling campaign to predict temporal effects on water geochemistry.
Stream water, as stream sediment, is always sampled upstream from bridges, artificial channels (culverts, flumes), and settlements (refer to Stream Sediment Sampling Chapter 3.4 and Sections §3.4.1 and §3.4.4 for information about selecting a suitable sampling site on a second-order stream).

## Slide 6
Important caution: Sampling sites should be located at least 100 m upstream from:
• Roads (dirt or asphalted)
• Railway lines
• Bridges
• Industrial sites
• Landfills (waste dumps), and
• Settlements
to avoid any potential anthropogenic contamination.

## Slide 7
3.3.2.1. Stream water samples to be collected
The following stream water samples are collected from a second-order stream:
(a) Routine sample site of a normal GTN grid cell:
1 x 500 ml bottle for unfiltered stream water for major IC ion analysis.
1 x 100 ml bottle for filtered stream water for ICP-MS and ICP-AES analysis.
1 x 100 ml bottle for mercury analysis, and
1 x 60 ml bottle for Dissolved Organic Carbon (DOC) analysis.
(b) Duplicate field site of a duplicate GTN grid cell (at least one in each country):
The same stream water samples, and field measurements, are taken at the duplicate field site (see below).
Sampling quantities: See bottle sizes above. However, before starting the stream water sampling campaign, the Project Manager should check with the laboratory the required volume for analysis.
Continued…..

## Slide 8
Duplicate stream water sample: Duplicate stream water samples are collected randomly at least at every 20th sampling site (i.e., ≈5% duplication of the sample sites) in each country.
However, countries with less than 6 GTN grid cells should collect field duplicate stream water samples from at least one random site.
The field duplicate stream water sample is collected from the same site less than five (<5) minutes after taking all field measurements (pH, electrical conductivity (EC), alkalinity).
3.3.2.1. Stream water samples to be collected
…..Continued…..

## Slide 9
3.3.2.2. Identifiers of stream water samples
The identifier of stream water samples is ‘W’:
(a) Routine sample site (e.g., GTN grid cell N26E14):
  Stream water sample: N26E14W1
Note: Number ‘1’ represents the 1st sample site in GTN grid cell N26E14.
(b) Duplicate field site (e.g., GTN grid cell N27E12):
  Stream water sample: N27E12W3
  Stream water sample – Duplicate: N27E12W3D
Note: Number ‘3’ represents the 3rd sample site in GTN grid cell N27E12, and ‘D’ denotes the duplicate stream water sample.
(c) Blank water sample: The identifier for a filtered blank water sample is zero (0),
i.e., GTN grid cell / W / sample no. / 0; for example, N27E12W30.

## Slide 10
Important note: The volume of stream water samples needed for analysis should be confirmed with the laboratory before purchasing the bottles. This is an issue that must be examined by the Laboratory Committee.

## Slide 11
3.3.3. Equipment for stream water sampling
As standardisation is very important in the project for the Establishment of the Global Geochemical Reference Network, the same equipment must be used by all countries and by all national sampling teams.
3.3.3.1. Equipment to be provided by the Project Coordinator
Certified trace element free bottles, disposable white-colour powder free vinyl gloves, disposable syringes, disposable syringe filters, droplet bottles, and black permanent drawing ink markers MUST be purchased centrally by the Project Coordinator and distributed to all participating countries.
3.3.3.2. Equipment to be purchased by each participating country
Each country must purchase the equipment that will be used in stream water sampling, and all sampling teams must have the same equipment.
Consult the Manual for the equipment needed for Stream Water Sampling.

## Slide 12
3.3.4. Stream water sampling procedure
It would be best if water sampling is carried out by persons who have practical experience in this procedure. Individuals, who are inexperienced in stream water sampling, should be trained for one to two weeks, and closely supervised for at least 10 days after the training programme to ensure that they follow the field sampling procedure, and safety precautions.
Calibration: The pH and electrical conductivity meters must be calibrated, according to the manufacturer’s instructions, at the start of each day.
Location of stream water sample: As the stream sediment sample is composited from 5 to 10 subsamples in the field (see Chapter 3.4), the stream water sample should be taken from the first, lowermost stream sediment sampling point.

## Slide 13
CAUTIONS:
All hand jewellery must be removed.
Samplers must not use insect repellent before sampling even when wearing gloves.
All tools and containers must be free of contaminants.
Note that the samplers are not allowed to smoke, or have the vehicle running when stream water samples are taken.
Avoid sampling during rainy periods and flood events.
The stream water sample must be taken before the stream sediment sample, for obvious reasons, i.e., during the collection of the stream sediment, fine-grained material is agitated and transported in suspension.

## Slide 14
Important caution during stream water sampling:
Do not touch anything except the stream water sample bottles upon wearing the powder-free disposable gloves.
Avoid glove and sample bottle contact with the ground or with human skin or clothing, and avoid breathing directly in the bottle or cap during sample collection.

## Slide 15
Important cautions:
Use disposable clean powder-free vinyl gloves and wear safety glasses, because the acid is very corrosive.
Do not let the droplet bottle or the tip of the pipette touch the sample of stream water in the bottle.
3.3.5. Treatment of stream water samples

## Slide 16
3.3.8. Photographic documentation of stream water sampling procedure
Figure 3.3.1 on page 222. Labelling bottles for stream water sampling by writing the sample number on each bottle with a black permanent ink marker, e.g.,
(a) Bottle for ICP-MS and ICP-AES analysis, and
(b) bottle for Hg analysis; similarly, the DOC is marked.
As the labels with permanent ink may be damaged during transport, it is recommended to be covered by transparent waterproof adhesive tape.
Photographs: Alecos Demetriades (IGME/IUGS-CGGB).

## Slide 17
3.3.8. Photographic documentation of stream water sampling procedure
Figure 3.3.2 on page 222. Wearing disposable powder-free gloves on both hands before the start of stream water sampling. Photographs: Alecos Demetriades (IGME/IUGS-CGGB).

## Slide 18
(a)
(b)
Figure 3.3.3 on page 223. Sampling unfiltered stream water sample for major IC ion analysis:
(a) Rinse 500 ml bottle with 50 to 100 ml of stream water, cap it and shake it, and
(b) Decant the stream water downstream of the sampling point; repeat the rinsing procedure a second time.
Sampling unfiltered stream water sample for major IC ion analysis
Continued…..

## Slide 19
…..Sampling unfiltered stream water sample for major IC ion analysis
(c)
(d)
(c) Submerge a 500 ml sample bottle completely, with its mouth facing upstream, and fill it up to its brim (i.e., completely full) with stream water in such a way that no air bubbles are left in the bottle, and
(d) Close the bottle by screwing the cap tightly below stream water level.
Almost the same procedure is followed by rinsing and filling up with unfiltered stream water the 100 ml bottle for Hg analysis, except that in this case the bottle is filled up to its neck leaving space for the addition of 5 ml HNO3-K2Cr2O7 stabilising solution.
Photographs: Alecos Demetriades (IGME/IUGS-CGGB).

## Slide 20
Cautions during stream water sampling:
If the stream is too shallow to immerse the bottle fully, submerge it at a low angle with the bottle mouth facing upstream, and with care not to touch the bottom sediment. If the stream is too shallow even for this procedure, then use the disposable syringe to fill up the bottle with stream water.
If the stream is too deep and fast flowing the water sample can be collected with a bailer device (Fig. 3.3.4).
This procedure can potentially agitate bottom sediment by stepping on a bank composed of loose material or loose rocks. So, extra care is necessary not to agitate bottom sediments during stream water sampling. It is, therefore, safer to use a bailer device for all occasions (Fig. 3.3.4), as the stream water samples can be collected by standing on the stream bank.

## Slide 21
Figure 3.3.4. (a) Fast flowing stream, Britannia Creek, British Columbia, Canada. (b-d) Stream water sampling with a bailer by Ray Lett. Photographs: Alecos Demetriades (IGME/IUGS-CGGB).
(a)
(b)
(c)
(d)

## Slide 22
(a)
(b)
Figure 3.3.5 on pages 224-225. Filtering stream water for ICP-MS and ICP-AES analysis (100 ml bottle). Rinse the disposable syringe two times with stream water:
(a) Fill up the disposable syringe with stream water, and
(b) Eject stream water downstream; repeat the rinsing procedure a second time.
Sampling filtered stream water sample for ICP-MS & ICP-AES analysis
Continued…..
…..Continued…..

## Slide 23
(c)
(d)
(c) Fill up the disposable syringe with stream water and
(d) Add 0.45 μm filter.
Continued…..
Sampling filtered stream water sample for ICP-MS & ICP-AES analysis
…..Continued…..

## Slide 24
(e)
(f)
(e) Discard downstream the first 10 ml of filtered stream water from each new filter used; rinse the bottle two times with filtered water by
(f) Adding 10 to 20 ml of filtered water in the bottle.
Continued…..
Sampling filtered stream water sample for ICP-MS & ICP-AES analysis
…..Continued…..

## Slide 25
(g)
(h)
(g) Close the bottle with cap and shake it rigorously, and
(h) Decanting the filtered water downstream.
Continued…..
Sampling filtered stream water sample for ICP-MS & ICP-AES analysis
…..Continued…..

## Slide 26
(i)
(j)
(i) Fill-up the bottle with filtered stream water, taking care for the filtered stream water to go straight into the bottle without any contact with your hands, and
(j) Close the bottle tightly with the screw cap.
Note: The bottle is filled up to its neck and room is allowed for the addition of 1.0 ml ultrapure nitric acid. Almost the same procedure is used for the collection of the filtered stream water for DOC analysis, but this time the 60 ml bottle is filled up to its brim. Photographs: Alecos Demetriades (IGME/IUGS-CGGB).
Sampling filtered stream water sample for ICP-MS & ICP-AES analysis
…..Continued…..

## Slide 27
Figure 3.3.6 on page 226. In the field, the stream water samples are stored in
(a) A car refrigerator,
and in the evening are stored in
(b) A refrigerator at a temperature <4oC.
Photographs: Alecos Demetriades (IGME/IUGS-CGGB).
(a)
(b)

## Slide 28
Figure 3.3.7 on page 226. Samples of stream water are packed in a strong carton box with insulating material boards (blue) in order to retain a low temperature during the transportation of the samples to the laboratory. Note: Addition of dry ice or ice cubes may be necessary, especially under hot environmental conditions. Photograph: Alecos Demetriades (IGME/IUGS-CGGB).

## Slide 29
3.3.9. Photographs to be taken at each stream/water sediment sampling site
Refer to Section §3.4.4.4. in Chapter 3.4 ‘Stream Sediment Sampling’ and Figure 3.4.20.
Figure 3.4.20 on page 250. Photographic documentation of stream sediment and stream water sampling site: (a) Sample number (remember the identification code of the stream water sample is used). (b) Landscape photograph N27E12W1L (21.62oE,39.96oN), and (c) Close-up of bedload material (N27E12W1S), FOREGS Geochemical Atlas of Europe, Hellas. Photographs: Alecos Demetriades (IGME/IUGS-CGGB).
(a)
(b)
(c)