## Slide 2
International Union of Geological Sciences
Manual of Standard Methods
for
Establishing the Global Geochemical Reference Network
Chapter 4
Sample Preparation and Storage
Daniela Mackovych1,3, Pavol Lučivjanský1, Alecos Demetriades2,3
1 State Geological Institute of Dionyz Stur, Regional Centre, Spiska Nova Ves, Slovakia
2 Institute of Geology and Mineral Exploration, Athens, Hellenic Republic
3 IUGS Commission on Global Geochemical Baselines
It is recommended that reference to this part of the Manual should be made in the following way:
Mackovych, D., Lučivjanský, P. & Demetriades, A., 2022. Sample Preparation and Storage. In: Demetriades, A., Johnson, C.C., Smith, D.B., Ladenberger, A., Adánez Sanjuan, P., Argyraki, A., Stouraiti, C., Caritat, P. de, Knights, K.V., Prieto Rincón, G. & Simubali, G.N. (Editors), International Union of Geological Sciences Manual of Standard Methods for Establishing the Global Geochemical Reference Network. IUGS Commission on Global Geochemical Baselines, Athens, Hellas, Special Publication, 2, 307−322.

## Slide 3
4.1. Introduction
The preparation of samples collected for the Global Geochemical Reference Network project should be prepared in a single, experienced and well-equipped facility. Demetriades (2014, p.2) stressed the significance of all stages of a geochemical mapping project, and particularly sample preparation: “Sampling is the costliest leg of the survey, and undoubtedly the most difficult to repeat if it is not carried out properly. The next step that must be performed correctly is sample preparation. Any mistakes made during sampling and sample preparation are difficult to trace and correct afterwards. As sampling and sample preparation affect project success, both must be carried out by well-trained personnel, and supervised by an experienced applied field geochemist and chemist, respectively. Laboratory analysis of samples is another costly part of the geochemical survey, and a stage of considerable concern. If samples, however, have been collected and prepared properly, they can be reanalysed until the results are of acceptable quality. Finally, data processing, map plotting, and interpretation, provided the previous stages of sampling, sample preparation, and analysis have given reliable results, are processes that can be repeated, depending on the skills of the applied geochemist.”
…..Continued…..

## Slide 4
4.1. Introduction
Since national restrictions for sending unprepared samples abroad may complicate the centralised sample preparation, direct negotiation with each country may be necessary at the start of the project, and before the sampling is completed. In the worst-case scenario where the sample preparation is to be carried out in the country of origin, the procedures described herein must be strictly followed and supervised by the Laboratory Committee of the IUGS Commission on Global Geochemical Baselines.
…..Continued…..

## Slide 5
4.2. Sample preparation equipment
The sample preparation laboratory should have the following equipment and packing materials:
• Temperature-controlled oven
• Unglazed porcelain mortar and pestle
• Jaw crusher
• Agate pulveriser with agate balls or agate rings (pulverisette)
• Sieving machine
• 0.063 mm sieve with nylon mesh fabric
• 0.150 mm sieve with nylon mesh fabric
• 2.0 mm sieve with nylon mesh fabric
• Polyvinyl chloride (PVC) sieve frame
• Rotary divider (splitter)
• Nylon brush
• Silica sand (to clean agate bowl and balls)
• Acetone
• Deionised water
…..Continued…..

## Slide 6
4.2. Sample preparation equipment
• Vacuum cleaner
• Powder-free single-use gloves
• Masks with filter
• White laboratory coat
• White laboratory hat
• Laboratory shoes
• 100 ml polyethylene bottles (PE) with colourless caps for analytical samples
• 200 ml PE bottles for archived samples
• Self-stick waterproof laboratory labels
• Black permanent ink marker
• Heavy-duty cardboard boxes for packing samples
• Computer and computer program for archiving samples
…..Continued…..

## Slide 7
4.3. Cleaning of sample preparation equipment
The sample preparation laboratory must be clean and dust-free.
All sample preparation equipment must be thoroughly cleaned before sample preparation commences.
Dust generated during the processing of samples should be vacuumed away through a dedicated filter system.
All sample preparation equipment must be thoroughly cleaned after each sample is packed to avoid contamination between samples.
4.4. Inspection of samples received
All sample sets received must be inspected, and catalogued and a ‘Bar code’ or ‘quick response’ (QR) code’ assigned for each sample for tracking the progress of its preparation.

## Slide 8
4.5. Randomisation of samples and insertion of control samples
Before starting the preparation of each sample set, the leading applied geochemist, or Quality Control Committee of the Global Geochemical Reference Network project, prepares a list of random numbers and sends it to the head of the sample preparation laboratory for implementation. This random list will allow the insertion of splits of the field routine-replicate samples (DUPA & REPA; Fig. 4.1) and their corresponding splits of field duplicate-replicate control samples (DUPB and REPB), project standard splits (secondary reference samples, SRMs) per batch of 20 samples, and a solid blank sample split per batch of 50 samples. Table 4.1 shows the insertion of 11 quality control samples in a randomised batch of 100 samples.
Ideally, the randomisation of samples should be done when all global project samples are collected.
If, however, it is decided to analyse collected samples, then they should be analysed in large, randomised batches of a few thousand samples (this action is not recommended).

## Slide 9
Figure 4.1 on page 312. Diagram showing the relationship between the field duplicate pair (DUPA and DUPB) and the laboratory replicate pair (REPA and REPB). Slightly modified figure from Johnson (2011, Fig. 5.2, p.64). Drawn with Microsoft™ PowerPoint by Alecos Demetriades, Hellenic Institute of Geology and Mineral Exploration (IGME) and IUGS Commission on Global Geochemical Baselines (IUGS-CGGB).

## Slide 10
Table 4.1 on page 313. Example of a random number list for sample number allocation to be used in the Global Geochemical Reference Network project: (a) Random number list showing the insertion of field duplicate (DUPA & DUPB) and laboratory replicate (REPA & REPB) pair sample splits, aliquots of two Global Geochemical Reference Network project SRMs (SRM 1 & SRM 2), and two aliquots of the solid Blank reference material (Blank 1A and 1B); the empty cells are then filled with routine Global Geochemical Reference Network project samples in consecutive numerical order. (b) When this batch of 100 samples is sorted in order of smallest to largest number, the samples are randomised. Table modified from Johnson (2011, Fig. 5.3, p.65).

## Slide 11
4.6. Sample preparation
Figure 4.2 shows the homogenisation and splitting into subsamples of all sample types that are to be collected during the Global Geochemical References Network project. The subsample splits in the 100 and 200 ml bottles of each sample type are weighed, and their weight recorded.
The inset in Figures 4.3 to 4.8 shows the balanced field duplicated-replicated sample design to explain the ‘additional splitting of duplicated field samples’, which are to be collected during the Global Geochemical Reference Network project. This is the balanced quality control of sampling and analysis scheme by duplicate-replicate sample splits, using analysis of variance (ANOVA), which was followed by the FOREGS Geochemical Atlas of Europe project (Sandström et al., 2005). It is strongly recommended that this balanced quality control scheme is used in the Global Geochemical Reference Network project.

## Slide 12
Figure 4.2 on 314. Diagram showing the homogenisation and splitting into subsamples of all sample types that are to be collected during the Global Geochemical Reference Network project. Ten 100 ml subsamples of each sample type are prepared for the analytical laboratories, and five 200 ml subsamples for storage. Drawn with Microsoft™ PowerPoint by Alecos Demetriades (IGME/IUGS-CGGB).

## Slide 13
Figure 4.3 on page 316. Rock sample preparation procedure.
Yellow-colour inset shows the additional splitting of field duplicate sample pairs in a balanced design.
Notation:
R = Routine field sample;
D = Field duplicate sample;
R1 & R2 and D1 & D2 are the laboratory replicate splits of the routine and field duplicate samples, respectively.
Drawn by Alecos Demetriades (IGME/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 14
Figure 4.4 on page 317. Residual soil sample preparation procedure (after Sandström et al., 2005, Fig. 4, p.86, with minor modifications).
Yellow-colour inset shows the additional splitting of field duplicate sample pairs in a balanced design.
Notation:
R = Routine field sample;
D = Field duplicate sample;
R1 & R2 and D1 & D2 are the laboratory replicate splits of the routine and field duplicate samples, respectively.
Drawn by Alecos Demetriades (IGME/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 15
Figure 4.5 on page 318. Humus sample preparation procedure (after Sandström et al., 2005, Fig. 5, p.87, with minor modifications).
Yellow-colour inset shows the additional splitting of field duplicate sample pairs in a balanced design.
Notation:
R = Routine field sample;
D = Field duplicate sample;
R1 & R2 and D1 & D2 are the laboratory replicate splits of the routine and field duplicate samples, respectively.
Drawn by Alecos Demetriades (IGME/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 16
Figure 4.6 on page 319. Stream sediment sample preparation procedure (after Sandström et al., 2005, Fig. 2, p.84, with minor modifications).
Yellow-colour inset shows the additional splitting of field duplicate sample pairs in a balanced design.
Notation:
R = Routine field sample;
D = Field duplicate sample;
R1 & R2 and D1 & D2 are the laboratory replicate splits of the routine and field duplicate samples, respectively.
Drawn by Alecos Demetriades (IGME/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 17
Figure 4.7 on page 320. Overbank sediment sample preparation procedure.
Yellow-colour inset shows the additional splitting of field duplicate sample pairs in a balanced design.
Notation:
R = Routine field sample;
D = Field duplicate sample;
R1 & R2 and D1 & D2 are the laboratory replicate splits of the routine and field duplicate samples, respectively.
Drawn by Alecos Demetriades (IGME/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 18
Figure 4.8 on page 321. Floodplain sediment sample preparation procedure (after Sandström et al., 2005, Fig. 3, p.85, with minor modifications).
Yellow-colour inset shows the additional splitting of field duplicate sample pairs in a balanced design.
Notation:
R = Routine field sample;
D = Field duplicate sample;
R1 & R2 and D1 & D2 are the laboratory replicate splits of the routine and field duplicate samples, respectively.
Drawn by Alecos Demetriades (IGME/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 19
4.7. Sample storage and management
The archived samples in the 200 ml PE bottles for long term storage must be stored in a secure and clean storeroom (Fig. 4.2). The PE bottles with the samples should have hand-written labels using a black permanent ink marker, as well as a specialised ‘Bar or QR code Tracking System’ to allow them to be quickly located.
The 10 splits of each sample type, prepared for sending to the analytical laboratories, will not necessarily be used immediately. Unused sample sets for analysis, which have been randomised and include the quality control samples, should be safely stored in a permanent clean facility, and be ready for despatch to a specified laboratory when the need arises.

## Slide 20
Temporary archive of the FOREGS Geochemical Atlas of Europe samples in Slovakia.

## Slide 21
Permanent archive of the FOREGS Geochemical Atlas of Europe samples at the British Geological Survey (https://www.bgs.ac.uk/geological-data/national-geological-repository/)