## Slide 2
International Union of Geological Sciences
Manual of Standard Methods
for
Establishing the Global Geochemical Reference Network
Chapter 7
Quality Control Procedures
Alecos Demetriades1,4, Christopher C. Johnson2,4, Ariadne Argyraki3,4
1 Institute of Geology and Mineral Exploration, Athens, Hellenic Republic
2 GeoElementary, Derby, United Kingdom
3 Department of Geology and Geoenvironment, National and Kapodistrian University of Athens, Hellenic Republic
4 IUGS Commission on Global Geochemical Baselines
It is recommended that reference to this part of the Manual should be made in the following way:
Demetriades, A., Johnson, C.C. & Argyraki, A., 2022. Quality Control Procedures. Chapter 7 In: Demetriades, A., Johnson, C.C., Smith, D.B., Ladenberger, A., Adánez Sanjuan, P., Argyraki, A., Stouraiti, C., Caritat, P. de, Knights, K.V., Prieto Rincón, G. & Simubali, G.N. (Editors), International Union of Geological Sciences Manual of Standard Methods for Establishing the Global Geochemical Reference Network. IUGS Commission on Global Geochemical Baselines, Athens, Hellenic Republic, Special Publication, 2, 387−428.

## Slide 3
Figure 7.1 on page 391. The triangular diagram shows how quality control procedures can contribute to two levels of the DATA + INFORMATION = KNOWLEDGE equation. Quality control produces the DATA set (verified geochemical results). This along with attribution of geochemical variability and measurement of uncertainty, plus other parameters such as threshold and normal background concentration determinations (INFORMATION) contribute to the KNOWLEDGE of the geochemical baseline and an understanding of environmental status, impacts and sensitivities. Plotted by Christopher C. Johnson (GeoElementary/IUGS-CGGB) with Microsoft™ PowerPoint.

## Slide 4
Figure 7.2 on page 396. Example of a control chart plot using QI Analyst software for the BGS Moroccan secondary reference material MB1 (after Johnson et al., 2001, Fig. 2.4, p.10). The central solid line represents the accepted value (AV) of the secondary reference material; outer black and olive colour dashed lines are at AV ± 2SD and ± 3SD, respectively. The red dot and line represent a batch that fails QC criteria. Source: Johnson (2011, Fig. 5.4, p.68).

## Slide 5
Figure 7.3 on page 396. Example of a control chart for a secondary reference material used in the EuroGeoSurveys URGE I project. The central solid line represents the accepted value (AV); outer dashed lines are at AV ±2SD and dotted lines at AV ±3SD. The secondary reference material was used in the urban geochemical mapping projects in different European cities, the results of which are separated by solid coloured lines. In some cases, the city samples were analysed in two different batches and at different times, and dashed lines separate the two batches. Plotted by Alecos Demetriades, Hellenic Institute of Geology and Mineral Exploration (IGME) and IUGS Commission on Global Geochemical Baselines (IUGS-CGGB) with Golden Software’s Grapher™ v20.

## Slide 6
Figure 7.4 on page 398. Duplicate-replicate plots for Cu and Ni for G-BASE urban soil (35-50 cm) from United Kingdom East Midlands. Axis units in mg/kg. Triangle = DUPA versus DUPB; Square= REPA versus DUPA; and Diamond = REPB versus DUPB (all x-axis versus y-axis). Notation: DUPA = Routine sample; REPA = Replicate split of routine sample; DUPB = Field duplicate sample; REPB = Replicate split of field duplicate sample. Source: Johnson (2011, Fig. 5.6, p.69).

## Slide 7
Figure 7.5 on page 400. The reduced major axis line is the best fit line of Y on X and X on Y. Source: Demetriades (2011, Fig. 6.2, p.82, slightly modified).

## Slide 8
Figure 7.6 on page 402. Variation of precision with concentration. Two examples of Be from the aqua regia GEMAS grazing land soil data set (Reimann et al., 2014) plotted with ‘IUGS-CGGB_Chapter-7_PDLPRECIS.xlsx’ Microsoft™ Excel file (see Supplementary material): (a) With negative values (N=94 pairs), and (b) With negative values removed (N=93 pairs). The former gives a PDL at 0.072 mg/kg and an overall precision of 18.4% at the 95% confidence level, and the latter a PDL at 0.046 mg/kg and an overall precision of 24.5% at concentrations beyond 50 mg Be/kg. Plotted by Alecos Demetriades (IGME/IUGS-CGGB).

## Slide 9
Figure 7.7 on page 403. Cumulative probability plots of Ni indicating true detection limits for topsoil samples determined by two different analytical methods (data from the FOREGS Geochemical Atlas of Europe – Salminen et al., 2005). Plotted by Alecos Demetriades (IGME/IUGS CGGB) with Golden Software’s GrapherTM v20.

## Slide 10
Figure 8.14 on page 450. Cumulative probability plot indicating true detection limits for samples determined by two different analytical methods. Such plots can demonstrate that the real detection limits (i.e., the point at the lower end of the cumulative distribution curve where the curve becomes horizontal) are often much lower than those cited by the analyst (the cited detection limits are marked on the plot). Recorded data for 10,000 samples from part of central and eastern England (from Johnson et al., 2018, Fig. 5.5, p.88).

## Slide 11
Figure 7.8 on page 404. Cumulative probability plots indicating that the conservative laboratory lower detection limits (LDL) of hot aqua regia extractable As and Tl for the agricultural (Ap) and grazing land (Gr) soil samples of the EuroGeoSurveys project of Geochemical Mapping of Agricultural and Grazing land Soil (GEMAS) of Europe, using uncensored data (Reimann et al., 2014), are higher than the true detection limits. In this case, the practical detection limit can be as low as 0.005 and 0.00009 mg/kg for As and Tl, respectively (Reimann et al., 2009). Plotted by Alecos Demetriades (IGME/IUGS CGGB) with Golden Software’s GrapherTM v20.

## Slide 12
Figure 7.9. A logarithmic-scale Thompson-Howarth plot was used for visualising analytical precision. This is a plot of G-BASE stream water duplicates for As with probabilities calculated at 0.2 μg/l detection limit using SigmaPlot v10 software by E.L. Ander (BGS). See AMC (2002) for the rationale behind the Thompson-Howarth plot. Solid, dashed, and dotted lines represent 99th, 90th, and 50th per cent confidence levels, respectively. Source: Johnson (2011, Fig. 5.7, p.71).

## Slide 13
Figure 7.10 on page 405. A normal linear scale Thompson and Howarth plot was used for visualising the precision of Pb. This is a plot from the results of the Hellenic Institute of Geology and Mineral Exploration's urban soil geochemistry project at Thrakomakædónæs, a suburb of Athens. Colour lines represent 10% and 20% precision at the 95% confidence level, and the 90th and 99th percentiles. Plotted by Alecos Demetriades (IGME/IUGS-CGGB) with Golden Software's Grapher™ v20.

## Slide 14
Figure 7.11 on page 407. (a) Balanced and (b) unbalanced hierarchical geochemical sampling and analytical schemes for the estimation of geochemical, sampling, and analytical variance and random components of measurement uncertainty. Source: Demetriades et al. (2014, Fig. 6.4, p.56) slightly modified.

## Slide 15
Figure 7.12 on page 411. (a) Histogram of Zn distribution with fitted normal distribution curve, and (b) Cumulative frequency plot of Zn in topsoil samples determined by XRF, FOREGS Geochemical Atlas of Europe (Salminen et al., 2005). It is noted that most of the topsoil samples have Zn concentrations <400 mg/kg. Plotted by Alecos Demetriades (IGME/IUGS- CGGB) with Golden Software's GrapherTM v20.

## Slide 16
Figure 7.13 on page 412. Cumulative frequency curves of Zn in routine and field duplicate topsoil samples determined by XRF, FOREGS Geochemical Atlas of Europe (Salminen et al., 2005). (a) Linear graph and (b) loge graph. Notation: DUPA = Routine sample; REPA = Replicate split of routine sample; DUPB = Field duplicate sample; REPB = Replicate split of field duplicate sample. Plotted by Alecos Demetriades (IGME & IUGS CGGB) with Golden Software's Grapher™ v20.

## Slide 17
Figure 7.14 on page 415. Duplicate-replicate plots for Zn from FOREGS Topsoil XRF quality control data (N=23 duplicated sites). It shows that the duplicate-replicate results are aligned close to the 1:1 gradient line. Plotted with ‘DUPREPPLOT.xlsm’, a Microsoft™ Excel Workbook macro routine developed by Christopher C. Johnson. Axis concentration units in mg/kg. Notation: Blue diamond = REPB versus DUPB; Red square = REPA versus DUPA; Green triangle = DUPA versus DUPB; and (all X-axis versus Y-axis). Notation: DUPA = Routine sample; REPA = Replicate split of routine sample; DUPB = Field duplicate sample; REPB = Replicate split of field duplicate sample. Plotted by Christopher C. Johnson (GeoElementary/IUGS-CGGB) with Microsoft™ Excel.

## Slide 18
Figure 7.15 on page 415. Duplicate-replicate plots for Th from FOREGS Topsoil XRF quality control data (N=23 duplicated sites). It shows a wide scatter of (i) Routine and field duplicate results (within site variability), and (ii) Duplicate-replicate results (analytical variability). Plotted with ‘DUPREPPLOT.xlsm’, a Microsoft™ Excel Workbook having an embedded macro routine developed by Christopher C. Johnson. Axis concentration units in mg/kg. Notation: See Figure 7.14. Plotted by Christopher C. Johnson (GeoElementary/IUGS-CGGB) with Microsoft™ Excel.

## Slide 19
Figure 7.16 on page 419. Multiple-boxplot of major element quality control data in European topsoil (N=23 duplicated sites). Plotted by Alecos Demetriades (IGME/IUGS-CGGB) with Golden Software’s Grapher™ v20.

## Slide 20
Figure 7.17 on page 419. Multiple-boxplot of trace element quality control topsoil data (N=23 duplicated sites; Total number of sample splits, N=92) – FOREGS project (Salminen et al., 2005). Plotted by Alecos Demetriades (IGME & IUGSCGGB) with Golden Software’s Grapher™ v20.

## Slide 21
Figure 7.18 on page 420. Multiple-boxplots of routine and field duplicate sample splits of (a) CaO and (b) Zn, FOREGS Topsoil QC data set (N=23 duplicated sites) (Salminen et al., 2005). The value of the upper whisker of all duplicate-replicate splits (N=92) is 1.63 wt% CaO, and 95 mg/kg Zn. Samples with values greater than these limits are considered outliers (see Table 7.1). Notation: DUPA = Routine sample; REPA = Replicate split of routine sample; DUPB = Field duplicate sample; REPB = Replicate split of field duplicate sample. Plotted by Alecos Demetriades (IGME/IUGS-CGGB) with Golden Software’s Grapher™ v20.
(a)
(b)

## Slide 22
Sample Number | CaO in wt% |  |  |  |  | Zn in mg/kg |  |  | 
 | DUPA | REPA | DUPB | REPB |  | DUPA | REPA | DUPB | REPB
N31E05T2 | 0.655 | 0.654 | 0.683 | 0.681 |  | 67 | 62 | 60 | 60
N37W04T4 | 0.128 | 0.129 | 0.119 | 0.121 |  | 11 | 10 | 15 | 12
N32E04T5 | 0.363 | 0.363 | 0.36 | 0.355 |  | 40 | 41 | 41 | 42
N34E07T3 | 0.963 | 0.964 | 0.976 | 0.981 |  | 93 | 91 | 95 | 94
N35E01T1 | 0.896 | 0.888 | 1.01 | 0.997 |  | 40 | 40 | 38 | 40
N37W01T4 | 0.027 | 0.026 | 0.023 | 0.022 |  | 1.5 | 1.5 | 5 | 1.5
N42E10T2 | 1.29 | 1.28 | 1.26 | 1.26 |  | 20 | 21 | 20 | 19
N43E09T4 | 1.22 | 1.22 | 1.34 | 1.33 |  | 13 | 9 | 15 | 13
N34E03T3 | 0.489 | 0.489 | 0.486 | 0.484 |  | 100 | 101 | 98 | 100
N32E01T1 | 0.337 | 0.337 | 0.257 | 0.256 |  | 30 | 31 | 32 | 34
N40E10T5 | 1.38 | 1.37 | 1.63 | 1.63 |  | 48 | 48 | 41 | 41
N33E08T5 | 0.23 | 0.232 | 0.234 | 0.232 |  | 22 | 23 | 23 | 26
N42E04T5 | 0.816 | 0.818 | 0.954 | 0.961 |  | 20 | 20 | 20 | 21
N43E04T5 | 3.29 | 3.29 | 3.10 | 3.10 |  | 50 | 49 | 37 | 31
N30E06T1 | 0.275 | 0.273 | 0.289 | 0.289 |  | 46 | 47 | 46 | 47
N38E04T4 | 0.549 | 0.55 | 0.539 | 0.548 |  | 27 | 26 | 24 | 25
N28E11T1 | 1.03 | 1.02 | 0.815 | 0.829 |  | 107 | 105 | 104 | 107
N34E10T5 | 0.147 | 0.149 | 0.11 | 0.110 |  | 17 | 19 | 19 | 19
N36E08T3 | 0.142 | 0.143 | 0.303 | 0.302 |  | 7 | 6 | 18 | 18
N31E03T4 | 1.59 | 1.57 | 4.46 | 4.47 |  | 50 | 50 | 46 | 47
N33E02T3 | 25.8 | 25.9 | 28.3 | 28.5 |  | 30 | 29 | 29 | 28
N34E01T1 | 1.03 | 1.04 | 0.566 | 0.57 |  | 34 | 37 | 30 | 32
N32E10T1 | 0.953 | 0.952 | 1.02 | 1.02 |  | 70 | 74 | 69 | 70
Table 7.1 on page 420. CaO (wt%) and Zn (mg/kg) results of routine and field duplicate sample splits of FOREGS Topsoil samples (Salminen et al., 2005). According to the results of the total number of samples (N=92), the outlying values for CaO are >1.63%, and for Zn >95 mg/kg. The outlying values are indicated by bold red numbers.
Notation:
DUPA = Routine sample;
REPA = Replicate split of routine sample;
DUPB = Field duplicate sample; REPB = Replicate split of field duplicate sample.

## Slide 23
Caption of
Table 7.2 on page 421 (next slide). Classical and robust analysis of variance results of CaO from the FOREGS Topsoil XRF data set (Salminen et al., 2005). Output as given by ROBCOOP4A.EXE program (Vassiliades, 2022). The coverage factor used in this case is 1.96 at the 95% confidence level.
Note: The output is exactly as given by the program. In practice, the results should not be quoted with more than two or three significant figures to the right of the decimal point depending on the number of integers.

## Slide 25
Caption of
Table 7.3 on page 421 (next slide). Classical and robust analysis of variance results of Zn from the FOREGS Topsoil XRF data set (Salminen et al., 2005) as given by the output of ROBCOOP4A.EXE program (Vassiliades, 2022). The coverage factor used in this case is 1.96 at the 95% confidence level.
Note: The output is exactly as given by the program. In practice, the results should not be quoted with more than two or three significant figures to the right of the decimal point depending on the number of integers.

## Slide 27
Figure 7.19 on page 422. Pie charts of robust balanced ANOVA results for (a) CaO and (b) Zn in topsoil samples of the FOREGS Geochemical Atlas of Europe, determined by XRF (Salminen et al., 2005). Plotted by Alecos Demetriades (IGME/IUGS-CGGB) with Golden Software’s Grapher™ v20.

## Slide 28
Figure 7.20 on page 423. FOREGS Geochemical Atlas of Europe maps of topsoil (a) CaO and (b) Zn determined by XRF. Source: Salminen et al. (2005, p.158 CaO -http://weppi.gtk.fi/publ/foregsatlas/maps/Topsoil/t_xrf_cao_edit.pdf; p.513 Zn - http://weppi.gtk.fi/publ/foregsatlas/maps/Topsoil/t_xrf_zn_edit.pdf). It is noted that the number of topsoil samples analysed by XRF is 845 and not 848.

## Slide 29
Measurement uncertainty and factor at the 95% confidence level |  | Calculation of LCL | LCL (mg/kg) | Calculation of UCL | UCL (mg/kg) | CI around measured value (mg/kg)
Robust expanded relative uncertainty (U') | 12.6% | 67 – (67*12.6%) (Equation 26) | 58.6 | 67 + (67*12.6%) (Equation 25) | 75.4 | ±8.44
Expanded uncertainty factor (FU) | 1.54% | 67/1.54 (Equation 34) | 43.5 | 67*1.54 (Equation 33) | 103 | -23.5, +36
Table 7.4 on page 422. Calculations using the Zn concentration of 67 mg/kg in topsoil sample N31E05T2 (see Tables 7.1 and 7.3) with respect to the robust expanded relative uncertainty (U΄=±12.6%), and expanded uncertainty factor (FU=1.54). The much higher UCL for the FU approach better reflects the positive skewness of the underlying logarithmic frequency distribution (see histogram and cumulative frequency curve in Fig. 7.12). The coverage factor used in this case is 1.96 at the 95% confidence level. See Table 7.5 for the calculations and Figure 7.21. Notation: LCL = Lower confidence limit; UCL = Upper confidence limit; CI = Confidence interval.

## Slide 30
Caption of
Table 7.5 on page 423 (next slide). Extract from the example used for plotting Figure 7.21 to show the calculations presented in Table 7.4 with respect to the Expanded uncertainty factor (FU). The Microsoft Excel worksheet is provided in the Supplementary material (IUGS-CGGB_Chapter-7_FOREGS_Topsoil_LCL_&_UPL.xlsx). Numbers were rounded to the first decimal place <99.9 and nearest integer >100.

## Slide 31
GTN Sample No. | Zni (mg/kg) ordered | Zni LCL (mg/kg) (Zni / FU%) | Zni UCL (mg/kg) (Zni * FU%) | Ei (mg/kg) (Zni * U´%) | Zni − Ei (mg/kg) | Zni + Ei (mg/kg)
 | Zni | Zni / 1.54 | Zni * 1.54 | Ei = Zni * 0.126 |  | 
……… | ……… | ……… | ……… | ……… | ……… | ………
N42E11T3 | 114 | 74.0 | 176 | 14.4 | 99.6 | 128
N25E13T1 | 115 | 74.7 | 177 | 14.5 | 101 | 129
N38W03T3 | 117 | 76.0 | 180 | 14.7 | 102 | 132
N32E07T1 | 118 | 76.6 | 182 | 14.9 | 103 | 133
N26E13T2 | 120 | 77.9 | 185 | 15.1 | 105 | 135
N30E06T4 | 130 | 84.4 | 200 | 16.4 | 114 | 146
N33E06T1 | 141 | 91.6 | 217 | 17.8 | 123 | 159
N29W02T5 | 142 | 92.2 | 219 | 18.0 | 124 | 160
N37W01T3 | 295 | 192 | 454 | 37.2 | 258 | 332
N31W01T5 | 314 | 204 | 484 | 39.6 | 274 | 354
N26E14T4 | 358 | 232 | 551 | 45.1 | 313 | 403
N27E05T1 | 396 | 257 | 610 | 50.0 | 346 | 446
……… | ……… | ……… | ……… | ……… | ……… | ………

## Slide 32
Figure 7.21 on page 424. Composite high-low-close plot of Zni versus Zni concentrations in topsoil samples showing the upper (UCL) and lower (LCL) confidence limits estimated by the robust expanded relative uncertainty (U′) and expanded uncertainty factor (FU) on the Zni concentrations. The most notable feature is the exhibited asymmetry of the UCL and LCL on the Zni concentrations calculated with the use of the expanded uncertainty factor (FU). It is noted that the plot shows Zn concentration values up to 400 mg/kg in the abscissa and 600 mg/kg in the ordinate. Plotted by Alecos Demetriades (IGME/IUGS-CGGB) with Golden Software’s GrapherTM v20.